## Slide 1: IPv6 in European Research Networks
Tim Chown (tjc@ecs.soton.ac.uk)
University of Southampton, UK
(European IPv6 Task Force, 6NET and Euro6IX projects)

## Slide 2: A quick tour of IPv6 in academia
IPv6 rationale for academia
IPv6 in research networks: GÉANT and 6NET
Network deployment
  Stability and performance for day-to-day use
  IPv6 network monitoring
Examples of IPv6 services
  Multicast, mobility, roaming, community networks,…
Applications, old and new
  Porting existing applications
  Developing new applications

## Slide 3: Why?
Research networks do not need a business case
  They provide and support research, on top of a production network
Teaching
  For students (particularly CompSci), projects, courseworks…
  Universities should teach leading edge technologies
  Put IPv6 where the brains are to breed innovation.
Research
  National and international projects and experiments
  Embracing related areas, e.g. Grid computing, Optical networking
It’s the Right Thing to do
Remember: The killer app for IPv4 took time to come

## Slide 4: IPv6 in universities
IPv6 has a role to play in enhancing education
We have heard many such ideas already this week
There are many users at home
  We see a huge growth in DSL use by staff and students
  This enables always-on, reasonable bandwidth to the users
  We should utilise this, e.g. for teleworking, collaboration
On campus information services
  New WLAN handhelds enable messaging, p2p, voice, etc.
  We will need MIPv6 to support campus-wide WLAN roaming
On campus infrastructure
  Various embedded systems, displays, sensors,…

## Slide 5: GÉANT, 6NET and the NRENs

## Slide 6: GÉANT and 6NET
All the European National Research and Education Networks (NRENs) are interconnected by GÉANT, offering a production IPv4 network service
  Many NREN plans are in sync with those of GÉANT
  NREN networks use a variety of hardware and technologies
GÉANT includes over 25 NRENs
  It will include more as the EU spreads to the east
  Technical IPv6 discussion in TERENA TF-NGN WG
  http://www.terena.nl/tech/task-forces/tf-ngn/
15 of the NRENs are members of the 6NET project
  6NET is a pan-European experimental research network project
  Has deployed a native IPv6-only network
  Funded in part by the European Commission

## Slide 7: GÉANT transition
GÉANT uses Juniper routers
Abilene (Internet2) runs Juniper routers
  Abilene migrated to dual stack in Autumn 2002
GÉANT roadmap
  Dual-stack was enabled in the backbone in Q1 2003
  Connecting the NRENs from Q2 2003
  Established native IPv6 connectivity to Abilene via dual-stack transatlantic links in May 2003
  Full production service end of 2003
    A service requires features such as full IPv6 management support.

## Slide 8: NREN transition
The NRENs wish to offer IPv6 services nationally
  Harmonised with IPv6 in the GÉANT core network
They need IPv6 address allocations
  Most NRENs have a production /32 prefix from the RIPE NCC
The NREN networks need to transport IPv6 – options include:
  Dual-stack networking
  IPv6 in IPv4 tunnels
  Parallel IPv6 network
  IPv6 over MPLS (where MPLS already exists)
  IPv6 with ATM (but ATM is now very rare in NREN networks)

## Slide 9: IPv6 address space
In Europe, IPv6 address space is allocated by the RIPE NCC
  Most NRENs have obtained a production IPv6 network address prefix (SubTLA)
  The prefix is a /32, e.g. JANET (UK) is 2001:0630::/32
  Each university site then receives a /48 prefix
  Thus an NREN can address 2^16 universities
  A site /48 prefix allows 2^16 site subnets to be allocated, with up to 2^64 (!) hosts per subnet (compared typically to 256 hosts now) - this allows administrators to easily resize subnets. It also deters port scanning.
Address allocation policies will be important
  A /48 per university seems a lot now, but in 5-10 years?

## Slide 10: Allocations of SubTLAs

## Slide 11: Dual-stack strategy
NRENs need an IPv6 transition strategy
  Need to be able to carry IPv6 on their infrastructure, and offer IPv6 services to end sites (universities)
  Help break the “chicken and egg” cycle
  Needs to be integrated with the university strategies
Can run IPv4 and IPv6 on the same router equipment, and run both protocols over the same links, natively
Requires vendor implementation to have fast (hardware-based) IPv6 forwarding, and to support the required IPv6 routing protocols (BGP4+)

## Slide 12: Dual-stack NRENs
Some NRENs have already migrated to dual-stack on their production networks, for example:
  SURFnet (Cisco) – the Netherlands
  FUnet (Juniper) - Finland
  Renater (Cisco) - France
  JANET (Cisco) - UK
  UNINETT (Cisco) - Norway
Most NRENs will make a dual-stack transition in 2003:
  Need confidence that IPv6 performance is as good as IPv4, and that IPv6 will not adversely affect the IPv4 service
  Examples of successful deployments breed confidence
  Academic deployment breeds robustness (through vendor feedback) for future commercial deployment

## Slide 13: IPv6 Land Speed Record
Promoted by Internet2 community
  http://www.internet2.edu/lsr/
Enables demonstration of IPv6 performance
Record recently set on network comprising GÉANT backbone and US link
  Ran on IPv4 production Juniper M20, M40, M160 routers
  Static IPv6 routes used
  Primary NREN sites RedIRIS and ARNES
  The result was as good as the IPv4 record at the time
Furthered the case for dual-stack on GÉANT in 2003
  Bolstered by experiences of Abilene Juniper network

## Slide 14: The LSR record confirmed…
IPv6 single stream record confirmed at I2 Fall Meeting in L.A. in October 2002
The next record…?

## Slide 15: IPv6 deployment at the edge
GÉANT and many NRENs have adopted IPv6 natively
They have high-performance native infrastructures
  e.g. JANET and GÉANT both widely10Gbit/s
This pushes native requirement to the edge
  i.e. to regional MANs and universities
Backbone deployment is in parallel to site-specific studies
  Deploying IPv6 in the enterprise network
  Will be largely dual-stack in the early phases
  New IPv6-only devices will appear in due course
The 6NET project is studying NREN and site transition

## Slide 16: The 6NET project

## Slide 17: The project
Deployed a pan-European IPv6 research network
  Backbone in place since May 2002 at STM-1 rates
Project runs until December 2004
  1,100 man months between 35 partner organisations
Many study areas beyond the underlying network rollout:
  Transition tools, MIPv6, DNS, QoS, address allocation policies, IPv6 multicast, IPsec, VPNs, multihoming, application porting, VoIP, Globus/GRID toolkit, multimedia tools, network management and monitoring,…
Desire to interconnect to international networks to further research goals through collaboration
  Including Abilene

## Slide 20: 6NET staging
Held in Brussels early in 2002, as part of Cisco Professional Services deployment

## Slide 21: 6NET results
6NET has 100 deliverables due during 2002-2004
  97 of those are public
  http://www.6net.org/publications/
Existing reports include
  MIPv6 implementations evaluation
  Network routing models (IS-IS, IPv6-only)
  DHCPv6 implementations evaluation (due soon)
  IPv6 transition technologies and cookbooks
  IPv6 application porting
  Network management tools (e.g. RIPE NCC TTM server)
  IPv6 deployment “missing pieces”

## Slide 22: IPv6 Network Monitoring

## Slide 23: Monitoring on 6NET
6NET weather map:
  http://netmon.grnet.gr/6net.html
  Relies on IPv6-only property for SNMP gathering
  Shows average flows, with MRTG plots
Working on IPv6 Netflow monitoring
RIPE NCC Test Traffic server
  http://www.ripe.net/ttm/index.html
  70 servers deployed, 10 now IPv6-enabled
  All new server shipped have IPv6 support
  Shows delays, packet loss between servers
  Includes historical traceroute records between servers

## Slide 24: Examples of IPv6 services

## Slide 25: IPv6 multicast - m6bone
A vehicle to gain IPv6 Multicast experience
  See http://www.m6bone.net/
Largely using tunnels (like the mbone for IPv4)
  Over 30 participants, from Europe and beyond
Has led to IETF Internet Drafts
  Multicast IPv4-IPv6 gateway (Stig Venaas, UNINETT)
  Embedded multicast RP address (Pekka Savola, FUNET)
Transitioning now to m6net
  Native IPv6 multicast on the 6NET infrastructure
  Limited to certain Cisco router line cards

## Slide 28: IPv6 Multicast applications
These include:
  Vic and Rat (conferencing tools)
  ISABEL (conferencing tool)
  Freeamp (MP3 streaming)
  MIM (MPEG streaming)
  ttcp and iperf (performance measurement)
Interesting challenge is to investigate implications of Source-Specific Multicast (SSM) for IPv6 on applications
  The IETF mboned Working Group believes PIM-SSM is the most architecturally clean way for IPv6 Multicast to move forward.

## Slide 30: Monitoring multicast
The m6bone runs an IPv6 multicast beacon
  Can monitor loss, delay and jitter
  Adapted from the NLANR beacon
  http://beaconserver.m6bone.pl/
We can also check the PIM-SM RP status
  Observed routes (unicast and multicast)
  Multicast groups, PIM-SM status

## Slide 31: Wireless LAN and IPv6

## Slide 32: Wireless roaming
The TERENA TF-Mobility Working Group is studying methods to allow WLAN roaming across European sites
  http://www.terena.nl/tech/task-forces/tf-mobility/
Solution space includes:
  802.1x (+ RADIUS)
  Restricted VPN access lists
  Web redirection to an authentication page (+ RADIUS)
Including a study of implications for IPv6
  How the above methods work (or do not!) with IPv6

## Slide 33: Community networking
Deploying WLAN access points in the community
  In a campus neighbourhood this offers outreach
Staff and students deploy access points with Linux routers
  Allows OSPF (for example) to be run on the network
Studying mesh network effectiveness over multi-hops
  Bandwidth drops off over multi-hop WLAN topologies
Studying how to address and route the network
  How to get an IPv6 address prefix to use on the mesh network
  How to select the external off-network link (if required)
  Use the nearest DSL site? Or pay for a fat(ter) ISP pipe?
Southampton Open Wireless Network
  http://www.sown.org.uk

## Slide 34: Applications

## Slide 35: Porting existing code
IPv6 API available in C and Java
Java Development Kit 1.4.1
  For Linux and Solaris
Best practice in porting being established:
  Making code IP (AF) independent
Documents:
  LONG: http://long.ccaba.upc.es/
  KAME: http://www.kame.net/newsletter/19980604/

## Slide 36: Applications
6NET is working on many applications
List is available online:
  Includes descriptions and IPv6 notes for each application
  http://6net.laares.info/
Also a fuller database of applications and patches:
  Can be searched by name or keyword, .e.g.”perl”:
  http://6net.iif.hu/ipv6_apps/
Key focus is to ensure that porting effort feeds back into the main development efforts
  Else we keep repeating the patching effort…

## Slide 37: Some 6NET examples
VOCAL
  SIP-based Voice over IP, open source code
  See http://www.vovida.org/
  Used on the 6WINIT project - http://www.6winit.org/
  Tested interop with other IPv6 SIP applications and gateways
Globus Toolkit
  Worked on version 2, now working on version 3
  Heavily Java based, using OGSA
  Ongoing effort within 6NET project
  First IPv6 meeting at concurrent Global Grid Forum

## Slide 38: Closing comments

## Slide 39: Conclusions
IPv6 is natively deploying in European research networks
  Almost exclusively through dual-stack deployment
Implications of IPv6 becoming better understood
  Updating services such as IPv6 multicast
  Network management and monitoring, running an IPv6 NOC
  New IPv6 features - e.g. IPv6 Privacy Extensions
Focus now is on applications
  Generating traffic, stimulating adoption
  Enhancing existing areas with IPv6, e.g. Grid computing
  Enabling staff and students to innovate in “6Wifi” environments
6NET has 18 months remaining to document best practice
  Various “cookbooks” being published at http://www.6net.org/